## Slide 1: mCNV Image Analysis
Progress so far

## Slide 2: Pipeline
Manually Cropped
Polygon Selection
Gaussian Blur
Sigma = 1
Frangi Filter
Spacing = [1,1]
Auto Local Thresholding
Method = “Mean”
Scale = [3, 5]
Radius= 8
Mexican Hat Filter
  Radius = 13
Skeletonize
Measure mCNV Area and Vessel Area, Vessel Density
Measure Vessel length and Junctions, Fractal D, Junction Density, V Diameter, Tortuosity

## Slide 3
Manually Delineated
Image
Gaussian Kernel
Denoising
(1A)
Hessian Frangi
Filter
(1B)
Median Thresholding (1C)
Mexican Hat
Filter
(2A)
Binary Skeletonization
(2B)
Scale: 170 Pixels/mm
Sigma = 1
Scale = [3, 5], Gaussian at each stage
Radius = 8
Radius = 13
8-bit Image
OCTA Image
Skeletonized Image

## Slide 4: mCNV Attributes
Measured Attributes
mCNV Area
Vessel Area
Vessel Length
Fractal Dimension
Vessel Junction
Derived Attributes
Vessel Density
Vessel Diameter
Junction Density
Vessel Tortuosity

## Slide 5: Function Parameters
The following Function parameters can be tuned to improve accuracy:
Function | Parameter | Current Value
Gaussian Blurring | Sigma | 1
Frangi Vesselness Filter | Spacing | [1, 1]
 | Scale | [3, 5]
Auto Local Thresholding | Method | “mean”
 | Radius | 8
Mexican Hat Filter | Radius | 13

## Slide 6: Sample Stages from Pipeline
1. Manually Cropped | 2. Gaussian Blurring | 3. Frangi Vesselness |  | 
 | 5. Mexican Hat Filter |  |  | 
7. Skeleton Analysis
6. Skeletonized
4. Auto Local Thresholding

## Slide 8: Attributes measured from Sample Image
mCNV Area (mA) (mm^2) | Vessel Area (vA) (mm^2) | Vessel Junctions (J) | Vessel Length (vL) (mm) | Vessel Density (= vA/mA) | Junction Density (= J/vL)
0.844 | 0.395 | 84 | 13.593 | 0.468009 | 6.179651
Similarly, a folder of images can be processed and the attributes can be written to a CSV file
The macros for doing this are written in ImageJ Macro Language (.ijm) and Python